## Slide 1: Auto-Calibration of HELIOS Data
2018-July-16th , Ryan Tang

## Slide 2: The Problem
Difference detector has difference gain, or MeV-to-channel
Manual or Semi-Manual method
Flatten e’ = a*z - e
Automatic method
Compare e(exp) with e(simulation)
(least square method)
Manually to find a
Set correlation = 0
align e’ for difference detectors

## Slide 3: Idea
Since the e-z plot is completely determined by kinematics
We can “map” the experimental plot to simulated plot
Challenge -- noise
Noise
Exp
Sim
~260 times smaller

## Slide 4: Algorithm – least square method
Pick a point in experimental data,
Scale the energy,
Find the point in simulation data,
  So that is minimum.
Obtain = Sum of all D.
Find the (a,b), so that is minimum.
  Monte Carlo Search
the threshold can discard the noise
User define parameters:
= 0.02
Search range for (a,b)
Monte Carlo trial

## Slide 5
Experimental Data
eThreshold
Origin data, not aligned

## Slide 6: Result
Accurate.
Well aligned.
Close to resolution of manual-Cali
Fast
6 mins
Origin data
1000 trials
e [a.u.]
e [MeV]

## Slide 7: Result – (e-z plot)
The resolution is as good as Manual.
Manual Calibration ( ~ few days)
Auto Calibration ( ~ few mins)

## Slide 8
Sigma : 65 keV
Ex ± 3 Sigma
Cut when solving () to (, )
small thetaCM
Manual sigma : 60 keV

## Slide 9: Advantage
Minimum Labor.
  Require a simple survey on the data before calibration.
No need to cut out small .
  auto-cut when “folded”
   ~5 deg (where it folded)
Fast
  Few days calibration  few minutes
Accurate
Folded

## Slide 10: map
= momentum of b or B in CM frame
= mass of proton
= beta for center of mass 4-vector
Solve for
The equation can be reduced to the form
= radial distance of the axis to detector
Solve for
= total energy in CM frame
= total energy of recoil particle in Lab frame
= mass of recoil particle

## Slide 11: Faster Searching Method – Random Walk
Search square
Search square
Search square
Size of search square reduced
No longer need.
But interesting to explore.