## Slide 1: Auto Calibration of HELIOS Data

## Slide 2: The Problem
Difference detector has difference gain, or MeV-to-channel
Manual or Semi-Manual method
Flatten e’ = a*z - e
Automatic method
Compare e with e_sim
(least square method)
Manually to find a
Set correlation = 0
Compare e’ for difference detectors

## Slide 3: Idea
Since the e-z plot is completely determined by kinematics
We can “map” the experimental plot to simulated plot
Challenge -- noise
Noise
Exp
Sim

## Slide 4: Algorithm
Pick a point in experimental data,
Scale the energy,
Find the point in simulation data,
  So that is minimum.
Obtain = Sum of all D.
Find the (a,b), so that 𝚺D is minimum.
  Monte Carlo Search
the threshold can discard the noise
Speed up trick: Sampling data.
User define parameters:
= 0.02
Search range for (a,b)
Monte Carlo trial

## Slide 5
Experimental Data

## Slide 6
runtime: ~ 6 mins,
~ 300 data point for experimental data
~ 200 data point for simulation data
#Monte Carlo trial = 60
ethreshold = 300
Slightly misaligned

## Slide 7: Result – (e-z plot)
The resolution is not as good as Manual.
  The scaling parameters are not the same for each detectors  the resultant slope of the e-z lines are not identical
Manual Calibration ( ~ few days)
Auto Calibration ( ~ few hours)

## Slide 8: Result – (Ex-z plot)
Strength the data for small thetaCM !
Cut when solving ( e,z) to (Ex, thetaCM)
If manual-Cali is using (e,z) to (Ex, thetaCM) mapping, could be improved.
Poor resolution: sigma = 100 keV

## Slide 9: Result – (Cos(thetaCM)-z plot)
If manual-Cali is using (e,z) to (Ex, thetaCM) mapping, Cos(thetaCM) could be done.

## Slide 10: Advantage
Minimum Labor.
  Require a simple survey on the data before calibration.
No need to cut out low thetaCM.
  auto-cut when “folded”
Disadvantage
Larger resolution

## Slide 11: Future improvement
Better searching algorithm
Find a method to fit same-pos detectors all together
  So that the scaling factor is the same
A easy mapping from (e,z) to (Ex, thetaCM)?

## Slide 12: (e,z) to (Ex, thetaCM) map
= momentum of b or B in CM frame
= mass of proton
= beta for center of mass 4-vector
Solve for
The equation can be reduced to the form
= radial distance of the axis to detector
Solve for
= total energy in CM frame
= total energy of recoil particle in Lab frame
= mass of recoil particle